RISC-V Rocket Chip Tutorials:
Adding a Peripheral

This is a tutorial to modify a rocket core running on a Xilinx Zedboard. This explains how to add peripherals, with the particular example being GPIO, to the AXI bus. This change allows control of the LEDs from the Rocket Core

Note: This Tutorial Requires Vivado

Adding LED GPIO as a Peripheral:
1. Open the project in Vivado
2. Using Vivado, open the block diagram
  1. This will be under rocket-chip wrapper. The file is called system.bd (block diagram)
3. Reconfigure/Edit AXI interconnect 1 to have 2 master interfaces
  1. Change number of master interfaces from 1, to 2
4. Instantiate an axi gpio
  1. Right-click→Add Ip
  2. Select axi-gpio
5. Run connection automation with the following settings:
  1. Attach gpio to led
  2. Be sure S_AXI is NOT selected
6. Rout GPIO S_AXI to M01_AXI on AXI interconnect 1
7. Rout clock and reset to clock and reset on each block
8. Connect M01 aclk and aresetn pins to the same lines they are connected to on M00
9. Open the address editor tab:
  1. Auto assign addresses
  2. NOTE: the offset address for gpio_0 is the base address of your pointer for accessing gpio from within a C program
10. Validate the design (F6)

Your new design can now be repackaged and sent to the FPGA